Title

---
Project Overview
- Special sort of ADC: ΣΔ
- Ongoing Project at IME
- Objectives: Measure, analyze, improve
- Focus in P5: test bench, measurement and data processing

---
System Overview
Source: Burgherr

---
Oversampling ADC
- Much higher fS than 2 × fNyquist
- Reduced demands on analog circuitry
- Increased demands on digital circuitry
- Yields additional bits of resolution
- Even better resolution with noise shaping:
  ΣΔ Modulators

---
ΣΔ Modulators: Noise Shaping
STF != NTF
Source: Carusone et al.

---
Test Bench
- Reliable results
- Prevention of user errors
- Efficiency
- Documentation
  Automation

---
Test Bench

---
Test Bench

---
Measurements

---
Pre-Amplifier

---
Pre-Amplifier Output vs Sampling Frequency
fs = 32 kHz
fs = 96 kHz
fs = 256 kHz

---
Pre-Amplifier Output vs Gain
Gain = 1
Gain = 8
Gain = 16
Gain = 4

---
First Order RC Model
Least-Squares fit with scipy.curve_fit()

---
Fitting the Model

---
Fitting the Model
fs = 256 kHz

---
Fitting the Model
- Tau 1&2
- DC voltage with offset

---
Pre-Amplifier Output vs Input
Gets worse

---
Tau vs Input Voltage

---
Tau vs Input Voltage
- Tau for fs=32 kHz is independent of gain
- Tau gets worse for higher fs
- Tau increases the more it deviates from Vref
  - gm decreases when Tau increases

---
Measuring Effective Gain
- Effective Gain
- Offset

---
Effective Gain vs fs, Chip, and configured gain

---
Sigma-Delta Modulator

---
Reconstructed Sine Wave from Bitstream

---
Reconstructed DC signal

---
Strange Outliers

---
Looking at the Time Axis

---
Linux and Time
- gettimeofday() is only ~10us accurate
- Use clock_gettime(CLOCK_MONOTONIC)
- Change niceness to -20 (high process priority)

---
Measuring Effective Gain & Offset
- Effective Gain
- Offset

---
Effective Gain & Offset
vs fs and chip

---
Whole System

---
Whole System: Gain & Offset

---
Questions